## Slide 1
STREAMFLOW
FORECASTING
MLP and LSTM models for daily river discharge
Methods, test results, and forecast limitations
Leaf River near Collins, Mississippi | 2003–2012

## Slide 2
What a daily flow forecast can support
STREAMFLOW FORECASTING
02
A forecast combines recent river flow and rainfall observations to estimate the next day’s discharge.
OPERATIONS
Reservoir planning and water allocation
PREPAREDNESS
Situational awareness during high flows
DECISION SUPPORT
A forecast is one input; local thresholds and observed conditions still matter
This project evaluates one station and one-day-ahead prediction; it is not a validated flood-warning system.

## Slide 3
Dataset and time-based evaluation
STREAMFLOW FORECASTING
03
3,653
daily records
2003–2007
training
2008–2010
validation
2011–2012
final test
USGS discharge
Leaf River near Collins, station 02472000; flow in cubic feet per second (cfs).
NOAA precipitation
Daily precipitation from the Collins, Mississippi station; rainfall in inches.
The 3,653-day count includes leap days. Chronological splits keep future years out of model fitting.
Notes: Sources: USGS station 02472000 https://waterdata.usgs.gov/ms/nwis/uv/?site_no=02472000 ; NOAA NCEI GHCN-Daily https://www.ncei.noaa.gov/products/land-based-station/global-historical-climatology-network-daily . Local project documentation reports the merged 2003-01-01 to 2012-12-31 period, 3,653 daily records, and year-based split.

## Slide 4
How the models were evaluated
STREAMFLOW FORECASTING
04
01
Split by year
Train 2003–07; tune on 2008–10; report final test on 2011–12.
02
Build lagged inputs
Use recent daily rainfall and flow values to predict next-day flow.
03
Tune and repeat
Choose settings on validation RMSE; retrain each neural model with five random seeds.
04
Compare fairly
Score persistence and linear regression on the same held-out periods.
Scaling uses training-set maxima only, according to the project script.
Notes: Method details verified against streamflow_project/streamflow_ann.py and EXPLANATION.md. Test set is not used for model selection. The five-seed mean is reported for neural networks; baseline results are single deterministic evaluations.

## Slide 5
Test-set error: MLP has the lowest RMSE
STREAMFLOW FORECASTING
05
RMSE (% OF MAXIMUM TRAINING FLOW)
Lower is better | test years 2011–2012
MLP
2.75%
LSTM
2.82%
Linear regression
3.06%
Persistence
3.23%
Mean over five neural-network seeds. MLP and LSTM rows show test RMSE as % of maximum training flow.
Notes: Source: local streamflow_project/reference_results/summary.json. Test means: MLP 2.7482%, LSTM 2.8237%, persistence 3.2319%, linear regression 3.0549%. The source deck’s 0.003 / 0.0035 values are not the saved test RMSE values and are removed because their metric and split were not identified.

## Slide 6
Test-set skill: neural models score higher on NSE
STREAMFLOW FORECASTING
06
NASH–SUTCLIFFE EFFICIENCY (NSE)
Higher is better | 1 is a perfect match
MLP
0.815
LSTM
0.797
Linear regression
0.771
Persistence
0.744
On this test period, both neural models outperform the two baselines on overall RMSE and NSE.
Notes: Source: local streamflow_project/reference_results/summary.json; test NSE values are means for five seeds for MLP and LSTM, and single evaluations for baselines. NSE compares model error to using the observed mean as the prediction; see Nash and Sutcliffe (1970), Journal of Hydrology 10:282–290.

## Slide 7
High-flow errors remain larger
STREAMFLOW FORECASTING
07
Peak RMSE is much higher than non-peak RMSE for every model.
Test RMSE (% of maximum training flow)
Peak days: observed flow > 1,500 cfs
MLP
8.16%
0.70%
LSTM
8.40%
0.59%
Linear regression
9.12%
0.72%
Persistence
9.65%
0.76%
Orange = peak RMSE Teal = non-peak RMSE
Notes: Source: local streamflow_project/reference_results/summary.json. Peak threshold 1,500 cfs per streamflow_ann.py. RMSE is reported as % of maximum training flow. Values shown are test means for neural models and baseline test values.

## Slide 8
Peak bias: neural models tend to underpredict
STREAMFLOW FORECASTING
08
Mean signed peak bias on the test set
Negative values mean underprediction; zero means no average signed bias.
MLP
-3.25%
LSTM
-6.63%
Linear regression
-9.11%
Persistence
-0.13%
Bias complements RMSE: persistence has near-zero average bias but the largest overall error.
Notes: Source: local streamflow_project/reference_results/summary.json, test peak_bias_pct. Neural-network figures are means across five seeds. Bias is defined in streamflow_ann.py as the mean relative error on peak days; negative means underestimation.

## Slide 9
Forecast limits and next steps
STREAMFLOW FORECASTING
09
What this experiment establishes
A one-station, one-day-ahead backtest on 2011–2012. Neural models improve overall error and NSE versus the included baselines.
What it does not establish
Reliable flood warnings, performance at other rivers, or multi-day forecast accuracy. The app’s recursive forecast feeds predictions forward and can accumulate error.
Next steps
Test additional stations and upstream predictors; evaluate multi-day forecasts with future rainfall inputs; report uncertainty and event-specific peak performance.
Treat these results as a project benchmark, not operational guidance.
Notes: Limitations are grounded in project scope and app.py forecasting behavior. The project documentation proposes multi-station and upstream predictors, probabilistic outputs, and real-time rainfall testing as future work.

## Slide 10
Sources and definitions
STREAMFLOW FORECASTING
10
Data
USGS station 02472000 — Leaf River near Collins, Mississippi
waterdata.usgs.gov/ms/nwis/uv/?site_no=02472000
NOAA NCEI — Global Historical Climatology Network Daily (GHCN-Daily)
ncei.noaa.gov/products/land-based-station/global-historical-climatology-network-daily
Project results and methods
Local project files: reference_results/summary.json, streamflow_ann.py, and EXPLANATION.md. All reported results use the saved project summary.
Metrics
RMSE is normalized by maximum training flow. NSE compares predictions with the observed mean. Peak days are defined as observed flow above 1,500 cfs.
Notes: Primary source details checked against USGS station page and NOAA NCEI GHCN-Daily official pages. Internal project files provide the exact data window, model procedures, and reported values.